## Slide 1
CAN PROTOCOL
(Controller area network)

## Slide 2: INTRODUCTION
CAN bus is a vehicle bus standard designed to allow microcontroller and devices to communicate with each other in vehicle.
It is a message based protocol.
It can send up to 8 bytes of data
It is present in both physical and data link layer of OSI layers.
It is a multi-master, multicast serial bus .
Standardized by ISO 11898-1, 11898-2
High Fault tolerance

## Slide 3: HISTORY
To reduce communication complexity on automobiles BOSCH starts work on CAN protocol in 1983, and official CAN released in 1986.
Intel/ Philips are the fist manufacture of CAN based microcontroller in 1987.
In 1991 CAN based first luxury car released by Mercedes Benz

## Slide 4: Before and After CAN

## Slide 5: CAN STRUCTURE
Dominant - 0
Recessive - 1
Dominant voltage level - 1.5v to 2.5v
Recessive voltage level - Above 2.5v

## Slide 6
WIRED AND LOGIC

## Slide 7: CAN with different layers in OSI model

## Slide 8: CAN FRAME FORMATS

## Slide 9: TYPES OF FRAMES
Data frame
Error frame
Remote frame
Overload frame

## Slide 10: Data frame
RTR - Remote Transfer Request
IDE - Identifier Extension Bit
DLC - Data Length Code
CRC - Cyclic Redundancy Check
EOF - End Of Frame

## Slide 11: CAN 2.0 B EXTENTED FORMAT

## Slide 12: Remote frame 11bit identifier

## Slide 13: Remote frame 29bit identifier

## Slide 14: ERROR FRAME

## Slide 15: Overload frame

## Slide 16: Interframe space

## Slide 17: TYPES OF ERROR
CRC Error
ACK Error
Form Error
Stuff Error
Bit Error

## Slide 18: CRC Error
NODE 2
NODE 3
NODE 1
CAN H
CAN L
CRC
CRC error flag
CRC error flag
ACK 0
ACK 0
1
0

## Slide 19
Form Error:
Form Error occur when recessive bits are changed as a dominant bit
Eg: End of frame, ACK delimiter, CRC delimiter , interframe space
Stuff Error:
Stuffing is a concept in communication Network to avoid the excessive DC component
Complementary bit added after 5 successive same bit

## Slide 20: Fault confinement
Active Error flag (continuous 8 dominant bits)
Passive Error flag
Bus off

## Slide 21
NODE 3
NODE 1
CAN H
CAN L
NODE 2
REC
TEC
REC
TEC
REC
TEC
Rt
Rt
1
0
1 bit error
000 000
000 000
8
20
11
21
16
12
1+8=9
Error echo
20
19
10
If REC or TEC <=128
It becomes a passive error
If REC or TEC <=256
It goes to bus off state

## Slide 23: Multi master arbitration Data frame
NODE 1 (11bit)
NODE 2 (11bit)
NODE 3 (29 bit)
NODE 4 (29bit)

## Slide 24: CAN ISOTP
A Classical CAN frame can carry maximum of 8 bytes of data
With ISO-TP:
The message is divided into multiple CAN frames and reconstructed by the receiver.
Types of ISO-TP Frames
Single Frame (SF)
First Frame (FF)
Flow Control (FC)
Consecutive Frame (CF)

## Slide 25: CAN ISOTP - Single Frame (SF)
Used when the message size is 7 bytes or less.
CAN Frame Structure
CAN ID
DLC
PCI
0x7E0
8
07
01
02
03
04
05
PCI (protocol control information)
PCI = 0x07
Lower Nibble = 7  Length Information
Upper Nibble = 0  Frame information
0x0X → Single Frame (SF)
0x1X → First Frame (FF)
0x2X → Consecutive Frame (CF)
0x3X → Flow Control (FC)
DATA (1 to 7 bytes)
06
07

## Slide 26: CAN ISOTP - First Frame (FF)
Used when the message is greater than 7 bytes.
Example : Suppose we want to send 20 bytes of data
CAN Frame Structure
CAN ID
DLC
PCI
0x7E0
8
0X10
14
01
02
03
04
PCI (protocol control information)
PCI = 0x10
Lower Nibble = 0  Length Information
Upper Nibble = 1  First Frame
The total message length is 12 bits, formed by combining:
Length = (Lower nibble of Byte0 << 8) | Byte1
Length = (0x0 << 8) | 0x14
= 0x014
Suppose the message length is 300 bytes.
300 Dec to Hex  0X12C
Byte 0 = 0X11
Byte 1 = 0X2C
05
06
Length
First 6 bytes

## Slide 27: CAN ISOTP - Flow Control (FC)
After receiving the First Frame, the receiver sends a Flow Control frame.
Purpose:
Allow or pause transmission
Specify how many Consecutive Frames may be sent
Specify the delay between frames
CAN Frame Structure
CAN ID
DLC
FS
Block
Size
ST
Min (ms)
0x7E0
03
30
04
0A
Flow Status (FS)
CTS(Continue to Send) - 0X30
Receiver :
Continue sending.
WT(Wait) - 0X31
Receiver:
Pause transmission and wait for next FC
Used when the receiver is temporarily busy.
OVFLW(Overflow) - 0X32
Receiver
My buffer is full.
Stop transmission (Abort)

## Slide 28: CAN ISOTP - Flow Control (FC)
Block Size
    Block Size controls how many Consecutive Frames the sender may transmit before waiting for another Flow Control frame.
Example :
Block size is 4
Sender
Receiver
CF1
Wait
CF2
CF3
CF4
FF
FC
FC
CF5
CF6
If BS = 0
The sender transmits all remaining CFs without waiting for another FC frames.

## Slide 29: CAN ISOTP - Flow Control (FC)
STmin (Separation Time)
STmin defines the minimum delay between two Consecutive Frames.
STmin specifies the minimum time the sender must wait between transmitting Consecutive Frames.
Example :
STmin = 5 ms
CF1
CF2
CF3
CF4
5ms
5ms
5ms
0x7E0
03
30
04
05

## Slide 30: CAN ISOTP - Consecutive Frame (CF)
After receiving FC, the sender starts transmitting the remaining data.
CAN ID
DLC
PCI
Data 0 to 7
0x7E0
8
21
01
04
03
05
06
02
07
PCI = 0x22
Lower Nibble =2  Sequence Number
Upper Nibble =2  Consecutive Frame
0x7E0
8
22
01
04
03
05
06
02
07
PCI = 0x21
Lower Nibble =1  Sequence Number
Upper Nibble =2  Consecutive Frame

## Slide 31: Example: Transmitting 40 bytes of application data using CAN ISO-TP
0x7E0 0x07 0x25 0x23 0x24 0x25 0x26 0x27 0x28
0x7E0 0x08 0x23 0x15 0x16 0x17 0x18 0x19 0x1A 0x1B
0x7E0 0x08 0x22 0x0E 0x0F 0x10 0x11 0x12 0x13 0x14
0x7E0 0x08 0x21 0x07 0x08 0x09 0x0A 0x0B 0x0C 0x0D
Sender
Receiver
CF1
CF2
CF3
CF4
FF
FC
FC
CF5
0x7E0 0x08 0x10 0x28 0x01 0x02 0x03 0x04 0x05 0x06
0x7E8 0x03 0x30 0x04 0x0A
10ms delay
10ms delay
10ms delay
10ms delay
0x7E0 0x08 0x24 0x1C 0x1D 0x1E 0x1F 0x20 0x21 0x22
0x7E8 0x03 0x30 0x04 0x0A
10ms delay
Transfer complete
Note :
If STmin = 5 ms:
Transmitting after 5 ms, 6 ms, or 10 ms is valid. Transmitting after 3 ms is not.